## Slide 1: Cache architecture improve computer performance with cache
I4GIC

## Slide 2: Motivation for caches
Motivation:
  Large memories (DRAM) are slow
  Small memories (SRAM) are fast
Make the average access time small by:
  Servicing most accesses from a small, fast memory.
Reduce the bandwidth required of the large memory

## Slide 3: An expanded view of the memory system

## Slide 4: Levels of the memory hierarchy

## Slide 5: The principle of locality
What are the principles of Locality?

## Slide 6: The principle of locality
The Principle of Locality:
  Program access a relatively small portion of the address space at any instant of time.
  Example: 90% of time in 10% of the code
Two Different Types of Locality:
  Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon.
  Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon.

## Slide 7: Memory hierarchy: principle of operation
At any given time, data is copied between only 2 adjacent levels:
  Upper Level (Cache) : the one closer to the processor
  - Smaller, faster, and uses more expensive technology
  Lower Level (Memory): the one further away from the processor
  - Bigger, slower, and uses less expensive technology
Block:
  The minimum unit of information that can either be present or not present in the two level hierarchy

## Slide 8: Memory hierarchy: terminology
Hit: data appears in some block in the upper level (example: Block X)
  Hit Rate: the fraction of memory access found in the upper level
  Hit Time: Time to access the upper level which consists of RAM access time + Time to determine hit/miss
Miss: data needs to be retrieve from a block in the lower level (Block Y)
  Miss Rate = 1 - (Hit Rate)
  Miss Penalty = Time to replace a block in the upper level + Time to deliver the block the processor
Hit Time << Miss Penalty

## Slide 9: Basic terminology: typical values

## Slide 10: How does cache work?
Temporal Locality (Locality in Time): If an item is referenced, it will tend to be referenced again soon.
  Keep more recently accessed data items closer to the processor
Spatial Locality (Locality in Space): If an item is referenced, items whose addresses are close by tend to be referenced soon.
  Move blocks consists of contiguous words to the cache

## Slide 11: The simplest cache: direct mapped cache

## Slide 12
Direct Mapped Cache
Direct mapped cache assigns cache mappings using a modular approach. Because there are more main memory blocks than there are cache blocks, it should be clear that main memory blocks compete for cache locations.
In direct mapped cache, a block of main memory has a specific location in cache.
For example, if cache contains 10 blocks, then main memory block 0 maps to cache block 0, main memory block 1 maps to cache block 1, . . . , main memory block 9 maps to cache block 9, and main memory block 10 maps to cache block 0

## Slide 13: Cache tag and cache index
Assume a 32-bit memory (byte ) address:
A 2N bytes direct mapped cache:
- Cache Index: The lower N bits of the memory address
- Cache Tag: The upper (32 - N) bits of the memory address

## Slide 15: exercise

## Slide 16: Definition of a cache block
Cache Block: the cache data that has in its own cache tag
Our previous “extreme” example:
  4-byte Direct Mapped cache: Block Size = 1 Byte
  Take advantage of Temporal Locality: If a byte is referenced, it will tend to be referenced soon.
  Did not take advantage of Spatial Locality: If a byte is referenced, its adjacent bytes will be referenced soon.
In order to take advantage of Spatial Locality: increase the block size

## Slide 17: Example
1 KB Direct Mapped Cache with 32 B Blocks
For a 2N byte cache:
The uppermost (32 - N) bits are always the Cache Tag
The lowest M bits are the Byte Select (Block Size = 2M)

## Slide 18: Block size tradeoff
In general, larger block size take advantage of spatial locality BUT:
  Larger block size means larger miss penalty:
  - Takes longer time to fill up the block
  If block size is too big relative to cache size, miss rate will go up
Average Access Time = Hit Time x (1 - Miss Rate) + Miss Penalty x Miss Rate